## Slide 1: EFFECT OF INSERT POROSITY ON COMBUSTION INSTABILITY IN A LEAN PREMIXED COMBUSTOR ANALYZED BY A POD-BASED PHASE RECONSTRUCTION TECHNIQUE
Mitchell A. Johnson, Ashley M. James, and Ajay K. Agrawal
2023 Turbo Expo, June 26-30, Boston, MA

## Slide 2: Background
Lean Premixed (LPM) combustion for power-generation gas turbines.
  Premixing facilitates globally lean, low temperature flames.
    Lower emissions of NOx, CO, and UHCs.
  LPM is vulnerable to thermoacoustic instabilities.
Swirl-stabilized combustion systems rely on recirculation zones to stabilize flame.
  Hot products feed back to reactants, initiate reactions.
  Combustor can become excited at certain frequencies to produce instability.
  Instability can be acoustically driven or result from other phenomena.

## Slide 3: Porous Inert Media (PIM) Insert
Previously, we have shown PIM’s effectiveness at mitigating thermoacoustic instability.
An annular ring of PIM is placed at the dump plane of the combustor.
PIM alters the flow/flame structures:
  Reduces jet divergence
  Eliminates recirculation zones
  Allows reactant flow through porous structure
  Produces flamelets to stabilize core flame
Although PIM is known to stabilize instabilities, questions remain about
  Role of porosity vs geometry.

## Slide 4: Objectives
Evaluate effects of insert shape and porosity in isolation.
  No insert
  Porous insert
  Solid insert
Examine details of combustion instability at a fixed equivalence ratio
  Acoustic probes
  Particle image velocimetry (PIV)
  OH* Chemiluminescence (OH*CL)
Apply POD analysis to assess differences in flow structure
Apply phase reconstruction to study differences in oscillation patterns

## Slide 5: Experimental Setup
Swirl-stabilized LPM combustor
  Optically-accessible flame tube
  Inlet swirl number of 1.5
Internal acoustic measurements were taken upstream of flame, in the mixing tube.
  Water-cooled PCB 106B, flush mounted, 40 kHz
Operating Conditions
  Air mass flow rate 1.02 kg/min (800 SLPM)
  Φ = 0.78 for detailed analysis

## Slide 6: Particle Image Velocimetry (PIV)
Image acquisition
  3500 image pairs per second
  16.7 μs between laser pulses
  Spatial resolution of 84 μm per pixel
Laser Sheet Optics
  F = 250 mm spherical lens
  F = -15 mm cylindrical lens
Seed
  1-2 μm silicon carbide
  Stokes number ~10E-6
1
2
3
4
5
7
6
SA-5
SA-5

## Slide 7: OH* Chemiluminescence (OH*CL)
1
2
3
4
5
7
6
SA-5
SA-5
Images acquired at 3.5 kHz
  Synchronized with PIV at 1 μs delay from the 2nd laser pulse
UVi Model 1850-10 intensifier
  750 ns exposure
  Filtered at 315 nm,
  15nm bandwidth

## Slide 8: Velocity Field Calculations
Two-pass recursive Nyquist grid
  Initial spot size 64x64 pixels
  Final spot size 24x24 pixels
FFT computes correlation function
  Peak found using bilinear peak finder
Three modes of validation
  Each pass – global and local median test
  Must exceed S/N ratio of 1.75
  Must not exceed 3 standard deviations away from local mean
~15% of vectors rejected
  Typically, in the area of two large laser reflections
  Results from low S/N ratio
Holes in data are recursively filled
  Preference given to holes with most valid neighbors
Results in vector field resolution of 1.36 mm / node.

## Slide 9: Total Acoustics Measurements
Three distinct regions in equivalence ratio.
φ = 0.75 to 0.78
  Solid insert and no-insert configurations destabilize.
φ = 0.70 to 0.74
  All three configurations behave similarly.
φ = 0.65 to 0.69
  Both inserts behave very similarly.
  Modest improvement on no-insert.
φ = 0.78 chosen for detailed analysis

## Slide 10: Time-Averaged Velocity Field
Porous Insert
  No flow recirculation
  Jet divergence reduced
Solid Insert
  Large recirculation zones
  High velocity diverging annular jet
No Insert
  Very large CTRZ
  Presence of central jet

## Slide 11: Acoustics Measurements
At φ = 0.78
  No insert and solid insert experience large amplitude pressure oscillations.
  Porous insert does not demonstrate large amplitude oscillations.
    Similar frequency of oscillation, but significant variability in waveform.

## Slide 12: Spectral Analysis of PIV and OH*CL Data
Solid insert experiences peak oscillations at 497 Hz
  Minor velocity peak near 300 Hz
No coupling in porous case
No-insert experiences peak oscillations at 309 Hz
  Minor second harmonic in OH*CL data.

## Slide 13: Proper Orthogonal Decomposition
Technique useful to isolate modes of oscillation in a fluctuating quantity u’.
Each mode consists of a temporal function a and a spatial function φ.
  φ describes on how u’ at a point in space correlates with every other point.
  a details how all points simultaneously oscillate in time.
Orthogonality dictates that data contained in one mode is duplicated in no other mode.

## Slide 14: PIV & OH*CL Modal Dynamics
Both modes contain significant oscillations at 497 Hz
Both modes incoherent
Significant LF activity in Mode 1
Both modes highly cyclical at 309 Hz
Unstable configurations concentrate far more of total oscillations in low-order modes

## Slide 15: No-Insert Modal Decomposition
Mode 2:
  Central recirculation zone velocity anti-correlated with flame locally
Mode 1:
  All jet velocities anti-correlated with flame activity
Stronger central recirculation zone enhances flame activity
Mode 1
Mode 1
Mode 2
Mode 2
Axial Velocity
OH*-CL emissions

## Slide 16: Solid Insert Modal Decomposition
Mode 2:
  Full field velocity is anti-correlated with core region of flame.
Mode 1:
  High velocity in downstream regions of jet at peak full-field OH* activity.
Again, central region of flow coupled with flame activity
Mode 1
Mode 2
Mode 1
Mode 2
Axial Velocity
OH*-CL emissions

## Slide 17: Porous Insert Modal Decomposition
Mode 2:
  Central flow region correlated with downstream flame
Mode 1:
  Velocity at outlet of insert core directly correlated to full-field flame activity
Flame oscillations notably absent from near field of porous surface
Mode 1
Mode 1
Mode 2
Mode 2
Axial Velocity
OH*-CL emissions

## Slide 18: Phase Reconstruction
We utilize time coefficients of POD modes for phase reconstruction
  If process is cyclic, this offers a way of overcoming cycle-cycle variations
  Signal noise complicates this process
  Thus, we filter data prior to POD to isolate structure of interest.

## Slide 19: No-Insert Phase Reconstruction
Diverging jet oscillates radially
As jet flow is reduced and shifts outward, recirculation zones expand
Strengthened flow recirculation enhances flame activity

## Slide 20: Solid Insert Phase Reconstruction
Diverging annular jet oscillates in length, velocity
Accompanying expansion and contraction of recirculation zones
Flame activity is enhanced by increasing recirculation zone strength

## Slide 21: High Resolution Phase Reconstruction – No Insert
At Z = 10 mm
  Jet Velocity and central recirculation zone velocity fluctuation together
  As diverging jet shifts inwards (θ = 180°), central jet weakens
    Central recirculation zone separates
  As diverging jet shifts outwards, vortex breakdown occurs
    Central recirculation zone split by central jet

## Slide 22: High Resolution Phase Reconstruction – Solid Insert
At Z’ = 20 mm
  As central recirculation zone strengthens, flame activity in core of jet begins to increase (θ = 0°)
  Overall velocity is impacted across combustor
    Result of jet interactions with standing acoustic wave
  Peak flame activity occurs directly after high-velocity region

## Slide 23: Conclusions
No-insert configuration experiences KH instability.
Solid insert eliminates KH-instability present in no-insert configuration.
  Still vulnerable to direct acoustic excitation.
Porous insert preserves effects of overall geometry.
Eliminating recirculation zones prevents acoustic coupling.
  Allows perturbations to convect downstream.
Recirculation zones not necessary for static flame stability.
  Flamelets on downstream porous surface act as pilot flames.
  This region is completely uncorrelated with major modal dynamics.

## Slide 24: Acknowledgements
This work was funded in part by NASA Grant NNX13AN14A.
Mitchell Johnson was supported by Graduate Assistance in Areas of National Need (GAANN) Fellowship Program.
The authors would like to thank James Allen and John Kornegay for their contributions to this work.