## Slide 1: Simultaneous Imaging of OH* and CH* Chemiluminescence in the Exhaust of a Rotating Detonation Engine
Ashley M. James and Ajay K. Agrawal
The University of Alabama
2024 Spring Technical Meeting of the Central States Section of The Combustion Institute

## Slide 2
Background
Chemiluminescence (CL): electronically excited radical formed by a chemical reaction.
CL Imaging
  Non-Intrusive, allows characterization of extreme environments without impacting the flow field or damaging sensors.
Species studied in hydrocarbon flames
  CH*: Indicates fuel breakdown, intensity peaks at rich conditions
  OH*: Indicates fuel oxidation, intensity peaks at stoichiometric condition.
CL intensities can vary with Equivalence ratio, Pressure, Temperature, etc.
Figure 1: Spectra of premixed methane flame.

## Slide 3
CL Imaging in RDEs
Figure 2: Rankin, Brent A., et al. [1]
Figure 3: Gaetano, Alec R., et al. [2]
Figure 4: Journell, Christopher L., et al. [3]

## Slide 4
Optical Setup
Light from the test media is emitted
  Split by a 50:50 beamsplitter
  Light is passed through each bandpass filter
    308nm OH*
    434nm CH*
  Filtered UV is reflected by the turning mirror onto the knife edge.
  Knife edge directs signal to the camera.
Camera
  Photron SA-5
  Invisible vision UV intensifier
Figure 6: Proposed optical configuration.
Bandpass Filter
To Camera
Beamsplitter
Turning Mirror
Turning Mirror
Bandpass Filter
Knife-Edge Prism
Aerospike
Outer Body
Annulus

## Slide 5
Superimposed
Optical Alignment
+X
+Y
A
B
C
D
E
A’
D’
E’
C’
A”
B”
C”
D”
E”
B’
1. Laser Alignment
2. Target Alignment
3. Resolution
Type: Rough Alignment.
Purpose: Addresses major mechanical misalignment.
How: Point spotting laser into apparatus at location of test media.
Pass/Fail: All point match without an indication of parallax.
Type: Fine Alignment.
Purpose: Addresses minor mechanical misalignment.
How: Set target at location of test media, take image and superimpose the right onto the left.
Pass/Fail: 90% or greater pixel alignment.
Type: Final/Focus/Resolution.
Purpose: Last alignment check, test image to acquire resolution and focus the camera.
How: Set ruler at location of test media, take image.
Pass/Fail: Any indication of misalignment.
Figure 7: Laser alignment target illustration.
Figure 8: Siemen Star target alignment.
Figure 9: Raw image of ruler for resolution.

## Slide 6
Annular Rotating Detonation Engine
Annular combustion chamber: fuel and oxidizer are fed into annulus annularly.
  100 mm OD
  80 mm ID
  139 mm height
Made of three concentric rings (spools)
  Joined together by through-bolts.
Center body that extends into an Aerospike
Figure 10: University of Alabama annular rotating detonation engine.

## Slide 7
Experimental Setup
High – Speed Camera
UVi Intensifier
Split Signal
Optical Apparatus
Optical Table
ROI
ROI
Figure 11: A) Region of Interest (ROI) , B) Optical apparatus in reference to engine , C) Image of experimental setup.
A)
B)
C)

## Slide 8
Test Parameters
Camera Settings
Test Conditions
Photron SA-5:
  50,000 fps
  Gate Time: 20 µs
  Image size: 512x272
    Or 0.158 mm/pixel
Uvi 1850-10
  Delay: 1 µs
  Gate: 18 µs
Equivalence Ratio: 1.0
CH4 Mass Flow Rate: 0.0673 kg/s
Oxidizer (2/3 O2 & Air): 0.386 kg/s
Total Mass Flow Rate: 0.454 kg/s
Heat Release Rate: 3.36 MW

## Slide 9
Broadband (unfiltered) CL Results
Identical wave illumination at location seen in both left and right sub-image.
Identical behavior observed in left and right space-time sub-image
  Wave seen approximately every 7-8 frames or .15 ms.
Figure 12: A) Video of Unfiltered Data, B) Space-Time plot.
B)
A)

## Slide 10
Data Validation: PCB versus CL Imaging
A)
B)
C)
Figure 13: A) PCB FFT/Spectrogram, B) Left sub-image FFT/Spectrogram , C) Right sub-image FFT/Spectrogram.

## Slide 11
Filtered Results
Clearly defined flow structure and reaction zone in the exhaust plume.
  Different intensity values based on individual species.
Various intensity observed in left and right space-time sub-image
  Wave seen approximately every 7-8 frames or 0.15 ms.
A)
Figure 14: A) Video of Filtered Data, B) Space-Time plot.
B)

## Slide 12
Data Validation: PCB versus CL Imaging
A)
B)
C)
Figure 15: A) PCB FFT/Spectrogram, B) OH* FFT/Spectrogram , C) CH* FFT/Spectrogram.

## Slide 13
Conclusions/Future Work
Implemented new optical setup to simultaneously image CL* and OH* CL in an RDE.
  Identical wave illumination/location seen in both left and right sub-image.
  The filtered results clearly show defined flow structure and reaction zone in the exhaust plume with different intensity values based on individual species.
  CL image results of FFT analysis and spectrogram match those obtained from PCB data.

## Slide 14
Questions?

## Slide 15
References
[1] Rankin, Brent A., et al. "Overview of performance, application, and analysis of rotating detonation engine technologies." Journal of Propulsion and Power 33.1 (2017): 131-143.
[2] Gaetano, Alec R., et al. "Comparative Analysis of Broadband Imaging and CH* Chemiluminescence for Ascertaining Modal Operation in a Rotating Detonation Combustor." AIAA SCITECH 2022 Forum. 2022.
[3] Journell, Christopher L., et al. "High-speed diagnostics in a natural gas–air rotating detonation engine." Journal of Propulsion and Power 36.4 (2020): 498-507.
[4] James, Ashley M., and Ajay K. Agrawal. "Spatially resolved chemiluminescence imaging of multiple combustion species using a single high-speed camera." Measurement Science and Technology 34.12 (2023): 125305.

## Slide 16
CL Imaging of Multiple Species
Common techniques used for simultaneous imaging
  Single Camera
  Two Cameras
  Image doubler
  Other optical arrangements
Present technique
  Utilizes an identical line of sight
  No need for extensive post processing and error correction
Figure 5: Line of sight conceptualization illustration.